## Slide 1: Machine Learning for Data Imputation, Real-time Reconstruction & Synthetic Data Generation in V2X Communication
Aditya Jawahar Kansara
08.07.2026, Kaiserslautern
Masters Thesis Presentation
Radio Communications and Navigation Department (WICON)
Supervisor: Prof. Dr.-Ing. Hans D. Schotten, M.Sc. Sanket Partani

## Slide 2: Agenda
Introduction
  Problem Statement
  Machine Learning for V2X Data
Berlin V2X Dataset
  Dataset Description
  Cellular dataset
  Data Analysis
Data Imputation
  Data Preparation
  Data Imputation Methods
  Evaluation and Results
Data Generation
  Purpose of Synthetic data
  Data Generation Methods
  Evaluation and Results
Conclusion & Future Work
  Intelligent Transportation System

## Slide 3
Introduction
1

## Slide 4: Introduction
A Vehicle-to-Everything (V2X) communication system consists of:
Vehicle-to-Vehicle (V2V)
Vehicle-to-Infrastructure (V2I)
Vehicle-to-Network (V2N)
Vehicle-to-Pedestrain (V2P)
These communication systems exchange information:
Vehicle Mobility
Network Quality
Traffic conditions
Communication Performance
V2N
V2V
V2I
V2P
Types of V2X Communication

## Slide 5: Introduction Problem Statement
A real-world operation of communication systems faces challenges such as:
Connectivity Interruptions
Unstable wireless conditions
Hardware limitations
Measurement Failures
Therefore, intelligent methods are required to reconstruct missing measurements and generate realistic communication data.
Challenges
Data Loss
Missing Values
Measurement Gaps

## Slide 6: Introduction Machine Learning for V2X Data
The structure of vehicle communication data is generally:
Highly Dense
Heterogeneous
Spatial and Temporally Dependent
Hence, we use advanced techniques like Machine Learning methods for handling communication data.
Machine Learning
Learn Temporal patterns
Handle Feature dependency
Generate or predict realistic data

## Slide 7: Introduction Machine Learning for V2X Data
The primary objective is to:
Fill up missing values in V2X dataset
Generate realistic data for missing measurement timestamps
                Selected Dataset  Berlin V2X Dataset
Why Berlin V2X?
Real-world measurement data
V2V and V2I Communication Data
Heterogenous features (GPS, traffic data, radio signal indicators, QoS data and weather data)
Suitable for studying signal fluctuations, time dependent behavior and missing values in V2X communication

## Slide 8
Berlin V2X Dataset
2

## Slide 9: Berlin V2X Dataset Dataset Description
Primary purpose: High resolution data of vehicle mobility and wireless network performance
4 Measurement Devices (Platoon, 2 x 2)
Urban Traffic conditions (residential streets, avenues, parks, tunnels,
  and highways)
Two Radio Access Technologies:
  Cellular Communication (V2I)
  Sidelink Communication (V2V)
Measurement route

## Slide 10: Berlin V2X Dataset Cellular Dataset
Real-world measurement of Vehicle communication over cellular (LTE) networks
Dataset shape: 207,434 rows x 159 columns
Data Category | Features
GPS | Latitude, Longitude, Altitude, Speed, COG, Area
Weather and Environmental | Temperature/apparentTemperature, precipProbability/ precipIntensity, dewPoint, humidity, windSpeed, cloudCover, uvIndex, visibility
QoS | Ping, Datarate, Jitter
Network Data | Signal Data: RSRP, RSRQ, RSSI, SNR RRC: Downlink/ Uplink frequency, Downlink/Uplink Bandwidth, Resource Blocks in Modulation and Coding Scheme(MCS), Cell ID/Cell Identity
Temporal Features and Identifiers | timestamps/ts-gps Device IDs Metadata (uplink, downlink, datarate/latency, scenario)

## Slide 11: Berlin V2X Dataset Data Analysis
The Cellular Dataset:
  159 raw features
  9 semantic groups
  Overall missingness (approximately 26%)
  Missingness neither uniform nor random
  Missing Pattern
    Missing Completely at Random (MCAR)
    Missing at Random (MAR)
    Missing Not at Random (MNAR)
Feature Group | #Feature | Avg. Missing % | Examples
Temporal | 2 | 0% | timestamp, ts_gps
Identifiers | 8 | 0-5% | device, operator, scenario, direction
GPS / Mobility | 7 | 1-2% | Latitude, Longitude, speed_kmh, COG
Weather | 11 | 1-2% | temperature, humidity, wind speed
Traffic | 3 | 1-2% | Traffic Jam Factor, Traffic Distance
Network QoS | 3 | 10-30% | datarate, ping_ms, jitter
PCell Signal | 21 | 5-15% | RSRP, RSRQ, RSSI, SNR
PCell DL / UL | 42 | 5-80% | MCS, RBs, TB Size, Tx Power
SCell Features | 53 | 70-100% | Secondary cell signal and radio data

## Slide 12: Berlin V2X Dataset Data Analysis
Feature Engineering
  Row removal: 1.2% of rows removed
     sensor initialization periods (no positional context)
  Data type correction: bandwidth columns
     text to numeric format
  Feature Removal:
    3 SCell features (100% missing)
    7 quasi-constant operator IDs
    1 redundant weather feature
    4 low-variance weather features removed
  MCS Aggregation: 32 MCS columns
     Low (QPSK), Mid (16-QAM), High (64-QAM/256-QAM)
  Log Transformation: 13 right-skewed features (datarate, ping, TB Size, RBs)  Normalization
  Missing Value Indicators: Binary flags to encode absence
  Categorical Encoding: One-hot encoding (device, area, direction, QoS mode); Binary encoding (operator)
  Temporal Features: Hour of day, Day of week
Data Cleaning

## Slide 13: Berlin V2X Dataset Data Analysis
Engineered Dataset
Baseline Imputation Methods
GRU-D
Completed Dataset
Baseline Data Generation Method
GRU-GAN
Synthetic Data Generation

## Slide 14
Data Imputation
3

## Slide 15: Data Imputation Data Preparation
Temporal split
Outlier clipping  (0.5th–99.5th percentile) to limit extreme values.
Feature Scaling  standardized using StandardScaler.
Artificial Masking: 15% of observed values randomly masked in validation and test sets.
   Used as ground truth to evaluate imputation accuracy using RMSE and MAE.
Split | Proportion | Training
Training | 70% (first in time) | Model parameter learning and scaler fitting
Validation | 15% (middle) | Hyperparameter tuning and early stopping
Test | 15% (last in time) | Final performance metrics (RMSE, MAE)

## Slide 16: Data Imputation Data Imputation Methods
Denoising Autoencoder
  For k=5, imputation by calculating mean of 5 similar observed values
  Capture cross-feature relationships
  Limitation:
    Cannot capture temporal dependency
    Treat each row independently
  Neural-network based approach
  Fully connected symmetric encoder-decoder
  Learns nonlinear cross-feature relationships by reconstructing clean data from corrupted(noisy) input
  Limitation:
    Limited performance on sequential V2X communication data
    Does not explicitly model temporal dependencies
Baseline: KNN Imputation

## Slide 17: Data Imputation Data Imputation Methods
GRU-D (Gated Recurrent Unit with Decay)
  RNN based  extension of traditional GRU model
    Ensure Temporal dependency of Sequential Data
  Missingness Mask (Informative Signal)
    A binary indicator is created for each feature  value (observed or missing)
    Fed directly into the model as an explicit input
  Time decay mechanism
    The longer a feature has been missing, the less the model relies on its last known value.
    GRU-D gradually shift toward the empirical mean as the gap grows.

## Slide 18: Data Imputation Data Imputation Methods
Time Gap δ(t) Time since last observed
Missingness Mask (m(t)) 1-observed, 0-missing
Feature Values (x(t)) Input Features
Update Gate
Reset Gate
Hidden State
Imputed Feature Values Current timestamp (t)
Forward Propagation
ReLU Activation
Dropout
Adjust input and previous hidden state
Input (per timestamp)
Temporal Decay
GRU Cell
Output Head
Hidden state (h(t-1)) feedback previous timestamp

## Slide 19: Data Imputation Evaluation Methods
Evaluation Metrics: RMSE and MAE
GRU-D achieves the best performance  improvement on signal quality features such as RSRQ, SNR, and RSSI where temporal structure is most critical.
Model | RMSE | MAE
KNN | 14771.35 | 41.12
DAE | 10.71 | 2.99
GRU-D | 5.45 | 1.80

## Slide 20: Data Imputation Results
The trained GRU-D model was applied to the complete dataset, successfully reconstructing all missing values across continuous features.
Feature | Missing Before | After GRU-D
Ping | 28.16% | 0%
Datarate | 7.65% | 0%
Jitter | 7.65% | 0%
PCell_Band_ Indicator | 6.15% | 0%
Key Outcomes:
  262,254 missing values imputed
     training, validation and test sets
  Final dataset: 204,942 rows and 72 columns
    no missing values remaining
  Completed dataset  input for the synthetic data generation pipeline

## Slide 21
Data Generation
4

## Slide 22: Data Generation Purpose of Synthetic Data
During the measurement campaign, all four devices experienced periods of measurement gaps.
A Generative model that is able to predict sequences and maintain temporal continuity is required.
 |  Observed gaps: | 
Device | Duration
pc1 | 20.2 mins
pc1 | 129.0 mins
pc2 | 11.5 mins
pc2 | 17.7 mins
The Problem
Gaps:
1.3 minutes to 2 hours
Standard imputation cannot fill these gaps
A generative model
   reconstruct complete measurement sequences
The Challenge
Signal features (RSRP, datarate, and ping) exhibit rapid fluctuations
The generated sequences must:
  Replicate behavior of signal features
  Preserve distribution characteristics
  Maintain temporal continuity
A conventional regression model predicts sequences
   overly smooth and regular.

## Slide 23: Data Generation Data Generation Methods
Simplest approach to autoregressive sequence generation is to use a LSTM network
Input
10 base context features + 38 target features at each timestep
Prediction
Predicts all 38 features simultaneously for the next timestep
Feedback Loop
Predicted values are fed back for next input
 repeated to generate a full sequence
Limitation
Generating all 38 features from shared hidden state cannot enforce the physical dependencies
GPS, cell configuration, signal quality, and QoS are all predicted at the same level.
   Produce feature combinations that cannot represent real-world measurements.

## Slide 24: Data Generation Data Generation Methods
The 38 target features are divided into five levels based on their physical dependency structure.
Level | Description | Example Features
1a | GPS Position | Latitude, Longitude
1b | Vehicle Mobility | Speed, Heading, Altitude
1c | Environment | Weather, Traffic
2a | Cellular Configuration | Frequency, Bandwidth
2b | Signal Quality & QoS | RSRP, SNR, Ping, Datarate
Vehicle position
cell connection
signal quality
cell configuration
QoS

## Slide 25: Data Generation Data Generation Methods
To achieve physical dependency and maintain statistical realism, a generative model that generates sequences resembling real values is required.
A Generative Adversarial Network (GAN)  uses a discriminator that penalizes unrealistic outputs.
GRU-LSTM: Different architectures for generator and discriminator prevent mode collapse.
Generator: GRU
Generate sequences  context features and preceding level outputs
Used across all five levels.
Discriminator: LSTM
Evaluates whether a sequence is real or generated
Output: a real or fake score by comparing to real data

## Slide 26: Data Imputation Data Generation Methods- Training Process
Seed Window:
20 real timestamp
Model parameters from each Level
Generator- GRU
Input
Level 1a- GPS
Base Context
Output L1a
Base Context Features (device, hour, day, direction, operator )
Generator- GRU
Level 1b- Mobility
L1a + Base Context
Output L1b
Generator- GRU
Level 1c- Environment
L1a + L1b + Base Context
Output L1c
Generator- GRU
Level 2a- Cell Config
L1a + L1b + L1c + Base Context
Output L2a
Generator- GRU
Level 2b – Signal & QoS
L1a + L1b + L1c + L2a + Base Context
Adversarial Training- GAN
LSTM Discriminator
Real Dataset
Generated Sequence
Feedback (Real or fake)

## Slide 27: Data Imputation Data Generation Methods
Seed Window:
20 real timestamp
Generated Sequence
Generator- GRU
Input
Level 1a- GPS
Base Context
Base Context Features (device, hour, day, direction, operator )
Generator- GRU
Level 1b- Mobility
L1a + Base Context
Generator- GRU
Level 1c- Environment
L1a +L1b + Base Context
Generator- GRU
Level 2a- Cell Config
L1a + L1b + L1c + Base Context
Generator- GRU
Level 2b – Signal & QoS
L1a + L1b + L1c + L2a + Base Context
The output from each level is passed to the next level
Output (GPS)
Output (Mobility)
Output (Environment)
Output (Cell Config)
Output (Signal & QoS)

## Slide 28: Data Generation Data Generation Methods
Generator adversarial loss: 0.782  2.148 Discriminator loss: 1.338  0.748.
Best model selected at epoch 30.

## Slide 29: Data Generation Evaluation Methods
GRU-GAN and LSTM models are evaluated on the held-out test set.
Limitation: LSTM performs better for slowly varying features such as temperature and GPS where the level-based structure provides less advantage.
Feature | RMSE | 
 | LSTM | GRU-GAN
Datarate | 1.787 | 0.562
Ping_ms | 1.302 | 0.564
PCell_RSRQ_max | 2.086 | 1.316
PCell_RSSI_max | 7.220 | 4.547
PCell_Uplink_Num_RBs | 2.338 | 0.690
Target_datarate | 2.470 | 0.339
Temperature | 0.387 | 1.925
Latitude | 0.006 | 0.011
Key Findings
GRU-GAN reduces RMSE by 21-86% for signal and QoS features
Level-based causal structure and adversarial training preserve natural signal variability.

## Slide 30: Data Generation Evaluation Methods
Evaluation discriminator is trained  Validate the generated sequences from GRU-GAN model
A score of 0.0926 means the classifier generated sequences that are statistically close to real measurements and difficult to distinguish.
Real Sequence
(V2X Dataset)
Evaluation Discriminator
(LSTM Classifier)
Classification
(Real or Generated)
Discriminative score
Initial model: 0.29 (78.26%)
Final Model: 0.0926 (59.26%)
Generated Sequences
(GRU-GAN)
Discriminative Score= |Accuracy – 0.5|
0.00 (perfect generation)  Cannot Distinguish
0.50 (worst result)  Easy to Distinguish

## Slide 31: Data Generation Results
Real vs Generated Feature-wise Data Distribution

## Slide 32: Data Generation Results

## Slide 33: Data Generation Results
GPS Data

## Slide 34: Conclusion
GRU-D effectively reconstructs missing cellular measurements
   Treat missing values in the V2X dataset
GRU-GAN generates statistically realistic synthetic sequences for missing timestamp intervals
A Discriminative score of 0.0926 confirms generated sequences are statistically close to real measurements
Future Work:
  Apply the pipeline to V2V communication datasets
  Extend generation to unseen routes and new timestamps beyond the training distribution
  Minimize error propagation for longer autoregressive sequence generation
  Adapt the pipeline for real-time deployment during live measurement campaigns

## Slide 35: Thank you!